## Slide 1: Fluctuating Power Logic: SCA Protection By VDD Randomization At The Cell-level
Fan Zhang, Bolin Yang, Bojie Yang, Yiran Zhang, Shivam Bhasin, Kui Ren
Notes: Hello everyone, my name is yangbolin and today I want to share the work which name is Fluctuating Power Logic. SCA Protection By VDD Randomization At The Cell-level.

## Slide 2: Content
1. Introduction
2. FPL scheme
3. Simulation
4. Conclusion
Notes: I will show this work in four parts and first is introduction

## Slide 3: 1. Introduction
Side-Channel Attack
Power dissipation correlates to switching operations using power models like hamming weight etc.
Major power consumption comes from the clock distribution network and Flip-Flops
(FFs) (estimated 30%-60%)
Notes: The SCA in the title means side channel analysis. And it cares about the power dissipation correlations with switching operations using power models like hamming weight
And it will lead to threats to information security
We investigated that Major power consumption comes from the clock distribution network and Flip-Flops (FFs) (about 30%-60% of the whole consumption is from FF
So our work concentrate on improving the flip-flops

## Slide 4: Mainstream SCA countermeasures
Hiding :noise, clock randomizer, dual-rail precharge logics
Masking: algorithm level, hardware level
Notes: There have some countermeasures to overcome the severe challenge of SCA. The two mainstream SCA countermeasures are hiding and masking.
Hiding means we can use noise, clock randomizer or dual-rail precharge logics to hide the dependence between the power consumption and data
And masking can de-correlate the dependency between the actual data and the power model by algorithm or some hardware model

## Slide 5: New countermeasure: FPL
Notes: The correlation of the three part is shown in the picture. The masking and hiding care more about the power model.
Our work aims to remove the correlation between key-dependent data and power dissipation directly, regardless of whether the power model is known to the adversary.

## Slide 6: Our contributions
We propose a novel cell-level logic: Fluctuating power logic(FPL)
We compared FPL with standard-cell-based and WDDL-based implementation
We analyzed side-channel security of FPL on PRESENT/AES implementation

## Slide 7: Content
1. Introduction
2. FPL scheme
3. Simulation
4. Conclusion
Notes: The second part let me introduce the FPL scheme

## Slide 8: 2. FPL scheme
The proposed logic is highlighted with a modified secure FF.
This scheme is based on a cascade voltage logic(CVL) and further enhanced with a compensatory unit (CU).

## Slide 9: cascade voltage logic(CVL)
n NMOS,
n diodes
one PMOS
one “n-input” OR-gate.
Vdp: voltage drop
Notes: the CVL unit is connected to VDD and a PRNG pseudo random number generator. consists of n NMOS and n diodes
Then it has one PMOS and one n-input OR-gate. The input of the OR-gate is controlled by PRNG
And the CVL unit will produce a OUTPUT named vddm to substitute the VDD with a random voltage drop.

## Slide 10: cascade voltage logic(CVL)
K=0 ,Vdp=0
K=1, Vdp=Vth0
K>1, 0<Vdp<Vth0
K denotes the total number of VMi whose logic value is “1”
Vth0 denotes the threshold voltage of NMOS and diode
Notes: To exactly know the value of the voltage drop, Let me use K denotes the total number of VMi whose logic value is “1” and also equal to the output of PRNG
If K equal to 0 all NMOS are shut off, the OR-gate output digital 0 and the output equal to VDD
K equal to 1 only one of Vmi equal to 1, the voltage drop equal to threshold voltage
If there are more than one Vmi equal to 1, the value of drop voltage will be between zero and threshold voltage
Depending on the values of VMi in the CVL unit, resulting in different discrete power consumptions for data transition in the whole FPL circuit.

## Slide 11: cascade voltage logic(CVL)
CP: circuit on critical path
NCP: circuit on non-critical path
Notes: The components in the original circuit C can be split into two parts, i.e.,those on and off the critical paths denoted as CPi and NCPi, respectively.
In order to avoid that the vddm influence the performance of the circuits, we just connect the vddm to non-critical path of the circuit and vdd is still connect to the critical paths

## Slide 12: Modified FF with FPL
Critical paths marked in brown
Non-critical paths marked in blue
Transistors connected with VDDm
marked in grey
Notes: the critical paths are marked in brown and those components off the critical paths which are connected with VDDm are marked in blue like pull-up unit, feed-back unit and so on

## Slide 13: compensatory unit (CU)
the power consumption for variant data transitions (0 →1 and 1→0) is larger than that for invariant ones (0→0 and 1→1)
When the FF makes a 0→1 or 1→0
the CU is off
when the inputs of FF keep unchanged
the CU is turned on
Notes: And we use compensatory unit to enhance the scheme. Because that the power consumption for variant data transitions (0 →1 and 1→0) is larger than that for invariant ones (0→0 and 1→1)
When the FF makes a 0 to 1 or 1 to 0 transition during the clock pulse window (tCLKp ), one of the pass-transistor gates controlled by D or DB is switched off while the other one outputs 0. So the CU is off.
Otherwise, when the inputs of FF keep unchanged, the CU is turned on, which consumes compensatory dynamic power during CLKp.
As aforementioned, the total power of FPL-FF (Ptotal) consists of three parts: the power of original FF (PFF ), the power of CVL unit
(PCV L) and the power of CU (PCU). So the randomness of power is derived from the uncertain sum of three parts relying on VDDm.

## Slide 14: Content
1. Introduction
2. FPL scheme
3. Simulation
4. Conclusion
Notes: The third part, we do some simulation for FPL scheme

## Slide 15: 3. Simulation
Testbench
compiling and synthesis by Design Compiler
n=4
HSPICE
Notes: For the purpose of illustration, only the case of n equal to 4 is applied and verified in the same test bench for both algorithms
compiling and synthesis by Design Compiler (DC)
In this simulation setup, all power traces are acquired from ideal digital circuits by detailed transistor level simulation through HSPICE
The applied experiment setup consists of two 4/8-bit input registers(Data, Key), one 4/8-bit output register, one 4/8-bit XOR gate and
the SBox module from the PRESENT/AES algorithms

## Slide 16: Simulation results
（GE）Gate equivalents
(SC-FF) standard-cell-based FF
(WDDL) dynamic differential logic
Notes: To be specific, the Gate equivalents (GE) of SC-, FPL- and WDDL-based testbench implementations are summarized in the first row of Table.
Pavg and P are the mean and standard deviation
We can see that, although FPL-based FF use more gates and power, but it performance is better than WDDL-based schemes.

## Slide 17: Comparation(AES)
Correlation vs. number of traces
Standard FPL
Notes: The simulation results are plotted here.
We compare standard AES implementation and FPL based AES implementation and these are correlation to number of traces
As you can see, in standard implementation, the correlation of the right key guess will appear using thirty traces
But in FPL implementation, it need at least two hundred traces.

## Slide 18: Comparation(AES)
Correlation vs. length of a trace
Standard AES PFL AES
Notes: these are correlation to number of a trace
We can see there is a obvious peak of correlation in standard implementation

## Slide 19: Comparation(PRESENT)
Correlation vs. number of traces
Standard FPL

## Slide 20: Comparation(PRESENT)
Correlation vs. length of a trace
Standard FPL

## Slide 21: Content
1. Introduction
2. FPL scheme
3. Simulation
4. Conclusion

## Slide 22: Conclusion
proposed a power-diffusing logic named as fluctuating power logic (FPL)
analyzed side-channel security on PRESENT/AES implementation
compared FPL with standard-cell-based and WDDL-based implementation